## Slide 1: Investigation of High-Capacity Digital Coherent Transceivers
Aimilios Christou, G&C College, ac2146

## Slide 2: Modeling the transmitter
Began by sending a collection of 10000 random symbols
Modulation with gray-mapped QPSK (Matlab function)
Adding random noise in amplitude and phase
Implementation of my own QPSK function to better understand the concept
Demodulation with Matlab-provided functions
Wk 1

## Slide 3
Noise and Demodulation

## Slide 4: Random Walk Noise and Noise Sets
Created different sets of noise
Each set is an order of magnitude larger than the previous one
This noise only affects phase
The cumulative sum function was used to model the phase noise as a random walk process
Wk 2

## Slide 5: Random Walk Noise and Noise Sets

## Slide 6: SNR and BER for Random Walk Noise
Plotting noise in a wrong way, bugs in code that need to be fixed
Attempting to measure noise with the snr Matlab function, cannot find the ratio between noisy signal and unfiltered signal correctly
Cannot find snr between symbols vector and their added phase noise vector either, approach replaced with specifying SNR directly instead of measuring it
Wk 3

## Slide 7: SNR and BER with AWGN
Repeating the transmission with AWGN noise gives the expected result.
Now two different noise models can be compared in further experiments
Created a known-symbol set instead of a random one for more control over the input

## Slide 8: Working towards a transceiver model
Wk 4

## Slide 9: Upscaling and FFT
Wk 5
Upscaled the symbols by 8, plotted the spectrum before and after modulation
Compared the spectrum with the spectrum of the symbols without upscaling
Learning about the Filter Bank method for spectrum plotting

## Slide 10: Chromatic Dispersion
Chromatic Dispersion Model:
C(exp(jωT )) = exp(−jK (ωT )2), Where K = Dλ2z/4πcT2
Chromatic Dispersion Filter:
Least Squares Filter:
Unable to implement ω as a vector correctly, do not know how to get the taps for an impulse response for the CD Model
Wk 6&7

## Slide 11: Pulse Shaping
Raised Cosine Filter with Interpolation/Decimation
Filter Parameters: Square Root, Roll off = 0.5, Taps: 32, Upsampling: 8
(looked at other filters: Nyquist)
Wk 8

## Slide 12: Need to Account for Delay in pulse-shaping filters
Delay is equal to N//2 where N is the number of taps used for a filter
> Using two filters (tx and rx) leads to a total delay of N taps
Therefore, need to shift output by N taps before demodulation
Winter Break

## Slide 13: Approach to Solution of Desynchronisation:
> First Implemented a direct shift by N which perfectly accounted for the delay. The problem with this approach is that other parts of the system also add delay and their delay is unknown. An approach that synchrosizes the TX and RX signal regardless of delay is needed.
> Synchronisation using cross-correlation has been implemented. The received downsampled signal after filtering with CD, AWGN and phase noise is correlated with the TX signal before pulse-shaping.
The Argmax of this cross-correlation is the delay between these 2 signals.
Problems:
This approach is not consistent and can also lead to values close to the true delay but off by 2-3 taps
Winter Break

## Slide 14: Diagram of Current Process
Create an array of 32K random symbols
Modulate with QPSK, with initial phase π/4 and gray coding
Filter with a pulse shaping filter1
Add AWGN
Add phase noise
Automatic gain control for normalization
Match filtering with a pulse shaping filter1
Demodulate from QPSK
Estimate BER, SNR and plot spectra
1Filter Parameters:
Upsampling/Downscaling = 8
Rolloff = 0.2
Tap Length = 32
Shape: Root Raised Cosine
Winter Break

## Slide 15: Diagram of Expanded Process
Create an array of 32K random symbols
Modulate:
QPSK, 16QAM, 64QAM
QPSK: initial phase π/4 , gray coding
Filter with a pulse shaping filter1
Add AWGN
Add phase noise
Automatic gain control for normalization
Match filtering with a pulse shaping filter1
Demodulate from QPSK, 16QAM, 64QAM
Estimate BER, SNR and plot spectra
Add Chromatic Dispersion
Resolve Chromatic Dispersion
Frequency Equalisation
Carrier Equalisation
FEC Encoding/Preamble
Decode using FEC
1Filter Parameters:
Upsampling/Downscaling = 8
Rolloff = 0.2
Tap Length = 32
Shape: Root Raised Cosine
Winter Break

## Slide 16: Things to be integrated after individual testing
Filter Delay (Done)
16QAM (Done)
64QAM (Done)
Chromatic Dispersion implementation and DSP filters to account for it (CD done, filters not working still, inverse CD does work)
FEC (LDPC using dvb s2 standard)
Carrier Equalisation (After FE)
Frequency Equalisation (Requires Local Oscillator Implementation – Ask)
Winter Break

## Slide 17
Winter Break

## Slide 18: Chromatic Dispersion Fix
Implemented a version of the CD Model that inverses its operation
This allowed for debugging to effectively check if the original model was implemented correctly
Now applying the CD Model and then the Inverse CD Model perfectly demodulates the signal. This means that the Linear and OLS Filters should properly attempt to correct for CD. This is still not the case.
Considerations of moving into personally implemented adaptive filters instead of Matlab-provided ones
Week 1-2 Lent

## Slide 19: Filter Taps Comparisons
Week 1-2 Lent
Implementation from lectures in the time domain
Implementation from lectures in the frequency domain

## Slide 20: Filter Taps Comparisons
Week 1-2 Lent
Modified Implementation from lectures in the time
domain to fix lecture note mistakes
Personal Implementation of FD-FIR Filter

## Slide 21: Carrier Equalisation
Adaptive Equalisation Methods
LMS, RMS filters. (MLSE as another option).
Resources lack implementation details, some pre-defined functions in MATLAB work for QPSK with AWGN, but could not be extended to equalise CD in QPSK or other modulation formats.
Alternative ways of Carrier Equalisation?
Need for Frequency Equalisation? (Requires implementation of non-linear effects, different polarisation for signals etc)