## Slide 1: Investigation of High-Capacity Digital Coherent Transceivers
Aimilios Christou, G&C College, ac2146

## Slide 2: Modeling the transmitter
Began by sending a collection of 10000 random symbols
Modulation with gray-mapped QPSK (Matlab function)
Adding random noise in amplitude and phase
Implementation of my own QPSK function to better understand the concept
Demodulation with Matlab-provided functions
Wk 1

## Slide 3
Noise and Demodulation

## Slide 4: Random Walk Noise and Noise Sets
Created different sets of noise
Each set is an order of magnitude larger than the previous one
This noise only affects phase
The cumulative sum function was used to model the phase noise as a random walk process
Wk 2

## Slide 5: Random Walk Noise and Noise Sets

## Slide 6: SNR and BER for Random Walk Noise
Plotting noise in a wrong way, bugs in code that need to be fixed
Attempting to measure noise with the snr Matlab function, cannot find the ratio between noisy signal and unfiltered signal correctly
Cannot find snr between symbols vector and their added phase noise vector either, approach replaced with specifying SNR directly instead of measuring it
Wk 3

## Slide 7: SNR and BER with AWGN
Repeating the transmission with AWGN noise gives the expected result.
Now two different noise models can be compared in further experiments
Created a known-symbol set instead of a random one for more control over the input

## Slide 8: Working towards a transceiver model
Wk 4

## Slide 9: Upscaling and FFT
Wk 5
Upscaled the symbols by 8, plotted the spectrum before and after modulation
Compared the spectrum with the spectrum of the symbols without upscaling
Learning about the Filter Bank method for spectrum plotting